## Slide 1
LAB 6
January 2025

## Slide 2: CONTENTS
01
02
03
Specification
Creating the Memory Design
Testing the Memory Design
04
Testing the Register Design
Achieved Outcomes.

## Slide 3
Specification
01

## Slide 4: 1. Specification
01
addr is a 5-bit logic vector. data_in and data_out are both 8-bit logic vectors. read, write, and clk are logic.
Memory write: data_in is written to memory[addr] on the positive edge of clk when write=1.
I/O interface
Notes: IC: Integrated Circuit

## Slide 5: 1. Specification
01
Memory read: data_out is assigned from memory[addr] on the positive edge of clk when read=1.
read and write should never be simultaneously high.
Notes: IC: Integrated Circuit

## Slide 6
Creating the Memory Design
02

## Slide 7: 2. Creating the Memory Design
01
Working in the lab06-mem directory, perform the following:
  For this lab, the memory design is already written (mem.sv).
        mem.sv top.sv
Notes: IC: Integrated Circuit

## Slide 8
Testing the Memory Design
03

## Slide 9: 3. Testing the Memory Design
01
You are going to complete the memory testbench in the mem_test.sv file.
You will be using the following SystemVerilog subprogram constructs:
  void function.
  Argument passing by name (.name(name)).
  Default formal arguments with default values.
Declare a task (write_mem) to write to the memory as follows:
  Define input arguments for the address and data values.
  Assign addr, and data_in from the arguments, and drive read and write synchronized to the clock. Hint: drive signals on the inactive clock edge to avoid race conditions.
  Define an input argument debug with a default value of 0. If debug = 1, display the write address and data values.
Notes: IC: Integrated Circuit

## Slide 10: 3. Testing the Memory Design
01
Declare a task (read_mem) to read the memory as follows:
  Define an input argument for the address value and an output argument for the read data. Remember to use blocking assignment for assigning read data to output argument, so that assignment is complete upon return to the caller.
  Assign addr from the argument, and drive read and write, synchronized to the clock. Hint: drive signals on the inactive clock edge to avoid race conditions.
  Assign the output data argument from data_out at an appropriate time. There is a short propagation delay between the rising edge of clk and data_out updating.
  Input argument debug with a default value of 0. If debug = 1, display the read address and data values.
Complete the “Clearing the Memory” test by writing zero to every address location, and then reading back and checking the data read matches the data written.
Complete the “Data = Address” test by writing data equal to the address to every address location, and then reading back and checking the data read matches the data written.
Write a void function (printstatus) with an input argument status which indicates the number of errors encountered in the tests. If status = 0, the test passed.
Notes: IC: Integrated Circuit

## Slide 11: 3. Testing the Memory Design
01
mem_test.sv
Notes: IC: Integrated Circuit

## Slide 12: 3. Testing the Memory Design
01
mem_test.sv
Notes: IC: Integrated Circuit

## Slide 13: 3. Testing the Memory Design
01
Run Command
  xrun mem.sv mem_test.sv top.sv
  The result as below:
Notes: IC: Integrated Circuit

## Slide 14
Achieved Outcomes.
04

## Slide 15: 4. Achieved Outcomes
01
  Understand the specification and create stimulus tasks using SystemVerilog subprogram enhancements and verify the supplied memory design.
  To use SystemVerilog subprogram enhancements to test a memory module.
Notes: IC: Integrated Circuit

## Slide 16
THANK YOU!