## Slide 1
LAB 9
January 2025

## Slide 2: CONTENTS
01
02
03
Specification
Creating the Simple Clocking Block Design
Testing the Simple Clocking Block Design
04
Testing the Register Design
Achieved Outcomes.

## Slide 3
Specification
01

## Slide 4: 1. Specification
01
The register is 8-bit rising-edge triggered, with asynchronous, active low reset.
                I/O interface
Notes: IC: Integrated Circuit

## Slide 5
Creating the Simple Clocking Block Design
02

## Slide 6: 2. Creating the Simple Clocking Block Design
01
Working in the lab09-cb directory, perform the following. The register is supplied in the file flipflop.sv together with a partial testbench in the flipflop_test.sv file.
Notes: IC: Integrated Circuit

## Slide 7
Testing the Simple Clocking Block Design
03

## Slide 8: 3. Testing the Simple Clocking Block Design
01
Modify the testbench:
  Add a clocking block whose clocking event is the rising edge of clk and which uses qin, reset, and qout for the clocking items.
  Use default skews of #1step for input and 4ns for output in the clocking block.
  Use cycle delays to drive the reset high and then low after 3 clock periods.
  Create a loop that drives new data on qin in every cycle via the clocking block.
Notes: IC: Integrated Circuit

## Slide 9: 3. Testing the Simple Clocking Block Design
01
Simulate the testbench and register design in GUI mode. View the register and clocking block signals (specifically qout and cb.qout) in a waveform viewer to see the timing behavior of the clocking block.
  xrun flipflop.sv flipflop_test.sv -access rwc -gui synchronyze and delay #4ns
    drive reset low after 3 cycle clock, synchronyze and delay #4ns delay and sample #1step
Notes: IC: Integrated Circuit

## Slide 10
Achieved Outcomes.
04

## Slide 11: 4. Achieved Outcomes
01
  Understand the specification and to use a testbench for a simple register to explore clocking block behavior.
  Simulate the testbench and register design in GUI mode and open waveform for tracing clocking block signals.
Notes: IC: Integrated Circuit

## Slide 12
THANK YOU!